## Slide 1
v
ME Team 68
Design of an Articulating Ankle for Enhanced Performance
Rachael Crow, Eric Brodeur, Kevin Cayo
Advisor: Dr. Jason Lee
MECHANICAL ENGINEERING
Sponsor: University of Hartford of Rehabilitation Sciences
Introduction/Motivation
Design/Methodology
Test Rig Setup
Design 1: Tension Spring & Elastic Band
Results & Analysis Design 1
Objective: Design and develop a functioning articulating prosthetic ankle that can be utilized both on land and in subsurface environments for rehabilitation purposes
Scope: Research, design, fabricate, and test an articulating ankle that allows for effective and comfortable use both on land and for SCUBA Diving without adjustment to ankle position when switching environments
Parties of Interest:
Transtibial amputees
Ex Military & Veterans
Metrics:
Ankle range of motion
Recovery & Down stroke
Critical Design Features:
Obtaining “ideal” ankle range of motion
  65 degrees from the vertical
Limit Energy Exertion
Weather and water resistant
Goal: Create a device that allows for a balanced stroke while not locked in a fixed position
  Prosthetic ankle produces similar stroke as able ankle - focus on recovery & down stroke
Inspirational Research
  Rampro “Swimankle”
  Nakashima Design
  Human Anatomy
Design Components:
  Spring Constant Range: .1 - 1.5 N/mm
    0.1 N/mm, 0.5 N/mm & 1.3 N/mm
  Elastic Band Length: 50.8 mm
    1, 5, 10
  Pin: 10.5 mm diameter
Initial Concerns:
  Longevity
    Solution - Decrease pin diameter
Attractions:
Previous research has been conducted
Variation of design has been used
Allows for variation in type of component used
  Spring or band
Motor Set Up:
1800 rpm motor
Gear box of 40:1 ratio
  Allowed for 45 kicks per minute
Motor stand to fit over the tank
  80/20 stand
Arm configuration
  2 aluminum pieces - 508 mm
  1 wooden piece - 1219.2 mm
  1 aluminum piece - 482.6 mm
    Key cut out for motor
attachment
    Hole location for wooden
arm connection
Tank Construction:
80/20 frame was used for frame
Plexi glass was used for the sides and bottom of tank
Water leakage prevention
  Gasket & Caulk
  Flex tape & Spray
Wooden supports
  Reduce bowing of plexiglass due to pressure of water
Rampro “Swimankle”
Initial Drawing
CAD Model
Drawing with Motor Set Up
Initial CAD Model
Initial Drawing
Motor & Gearbox
Final Design - Rubber Band
Final Design
Final Design - Tension Spring
VS.
Strongest recovery stroke
  Narrowest peak
Weakest downstroke
  Lacks full ankle extension
Good downstroke
  Near full extension of foot
Good recovery stroke
  Narrow peak
Most balanced design of three tension springs
Weakest recovery
  Thickest peak
Strong downstroke
  Full ankle extension
Ankle Joint
End of Prosthetic Foot
Notes: Flow is important: why is the project here, methodology (why we decided on our designs), rig, designs, comparison
Problems and how we overcame them!!!
dorsi to plantar, downstroke, plantar to dorsi, upstroke
Break down:
Introduction/motivation - Rachael
Methodology
  Goals & prior research w Nakashima & rampro - Rachael
  human anatomy - Kevin
  Design & analysis motivation - Eric and Kevin
Test Rig Setup - Kevin
  Problems encountered - Rachael
Design 1 & 2 & Analysis - Eric
Design 3 - Kevin
Design comparison - Eric
Conclusions & Recommendations - Rachael
One oscillation is 1.33 seconds because 45 oscillations per minute.
one oscillation is 40 frames at 30 fps

## Slide 2
v
MECHANICAL ENGINEERING
Design 2: Torsional Spring
Results & Analysis Design 2
Design 3: Ball & Joint
Design Comparison & Final Design
Conclusions & Recommendations
ME Team 68
Design of an Articulating Ankle for Enhanced Performance
Rachael Crow, Eric Brodeur, Kevin Cayo
Advisor: Dr. Jason Lee
Sponsor: University of Hartford of Rehabilitation Sciences
Design Components:
  Max Torque Range: 250 - 650 N*mm
    258.74, 268.93, 383.02, 508.43, 623.45
  Pin: 10.5 mm diameter
Initial Concerns:
  Overextension
    Solution - Add pin to limit range of motion
Attractions:
Most sleek & compact design
Generates a lot of torque to help with recovery stroke
Design Components:
  Lubricant: Oil or putty based
  Elastic Band: 50.8 mm
Initial Concerns:
  Lubrication Dissipation
    Solution - Use of putty lubricant
Attractions:
Most human like
Larger range of motion
UConn: Jason Lee, Vito Moreno, Thomas Mealy
Sponsor: Duffy Felmlee & Stephen Charry
“Activankle & Swimankle, Prosthetic Ankle Joints for Swimming, Jet/Snow Skiing, Rowing.” Rampro, https://www.rampro.net/ .
“Journal of Biomechanical Science and Engineering.” Development of the Transfemoral Prosthesis for Swimming Focused on Ankle Joint Motion, vol. 8, no. 1, 2013, p. 93. Journal of Biomechanical Science and Engineering, https://www.jstage.jst.go.jp/article/jbse/8/1/8_79/_pdf.
Acknowledgements
References
Initial Drawing
Initial CAD Model
Initial CAD Model
Initial Drawing
Conclusions
  Torsion spring 3 performed best with ankle range of motion
  Tension spring 2 produced the most balanced stroke out of design 1 & torsional spring 3 produced the most balanced stroke out of design 2
    Torsional spring 3 performed better in terms of downstroke
    Tension spring 2 performed better in terms of recovery stroke
  Flipper deflection was inconclusive
    Require a larger tank with slower arm oscillation
  Can create a design that doesn’t require position adjustments
Recommendations
  Complete Human Testing
    Focus on quantitative & qualitative metrics
      Flipper Deflection & ankle range of motion
      SWOLF, pace, heart rate, & comfortability
  Pursue finding “ideal” spring constant for tension spring design
  Fabricate and test Ball & Joint Design
Final Design
Strongest recovery
  Narrowest peak
Weakest downstroke
  Ankle not fully extended
Satisfactory recovery
  Slightly thicker peak
Good downstroke
  Almost full extension of ankle
Less powerful recovery
  Thicker peak
Strong Downstroke
  Full extension of ankle
Weaker recovery
  Thicker peak
Stronger Downstroke
  Full extension of ankle
Weakest recovery
  Thickest peak
Strongest Downstroke
  Full extension of ankle
  Closest path to ankle range of motion
Tension spring iteration 2 and torsion spring iteration 3 had the best balance of their respective springs
Torsion design had a stronger downstroke with a fully extended ankle while tension design had a better recovery
Able ankle has longer downstroke and shorter upstroke because of required energy and drag
Could not simulate because powerful motor generated constant oscillation & no flipper use in test rig testing
Torsional spring design has a more similar downstroke while tension spring design has a more similar upstroke
Both have same recovery angle as able foot
Notes: go through designs after test rig set up and then discuss analysis and comparison after it
IRB takes time - requirement of processing for human subject testing
Can have graphs in one area (each design has a graph comparing their own iterations, pick the best one to compare in overall comparison area) and explain in comparison area